## Slide 1
NON-DESTRUCTIVE TESTING

## Slide 2: What is NDT?

## Slide 3: What is NDT?
Non-Destructive Testing: Methods to analyze the properties and structures of materials without damaging the components being evaluated.
Also known as:
  NDE (Non-Destructive Evaluation/Examination)
  NDI (Non-Destructive Inspection)

## Slide 4: What are some of the defects we try to detect?

## Slide 5: What are some of the defects we try to detect?
  Cracks
    Heat stress
    Shrinkage
    Hydrogen
  Porosity
    Welding
    Casting
  Lack of fusion
  Solid Inclusions
  Cold shuts
  Lack of penetration
  Laps or seams
    Wrought processing

## Slide 6: What industries use NDT?

## Slide 7: What industries use NDT?
  Aerospace
  Marine (propellers)
  Nuclear
  Infrastructure
  Petroleum

## Slide 8: NDT Levels of Qualification
Level 1:
  Ability to perform specific calibrations, tests, and evaluations according to written instructions.
Level 2:
  Ability to setup and calibrate equipment, interpret and evaluate results in accordance with codes, standards, and specifications. Report results.
Level 3:
  Establish techniques, interpret codes, designate test methods and techniques used. Possess practical background in technology and familiarity with methods of NDT.

## Slide 9: What are some of the methods?

## Slide 10: What are some of the methods?
  Visual Inspection
  Leak Testing
  Magnetic Particle
  Dye Penetrant
  Ultrasonic
  Eddy Current
  Radiographic

## Slide 11
Introduction to Ultrasonic Testing
Medical Application
Industrial Application

## Slide 12: Ultrasonic inspection is used in many applications to ensure product safety and reliability.

## Slide 13: What is ultrasound and how does it work?
Ultrasound waves are acoustic energy above the human hearing range.
The human ear can detect sounds of up to 20,000 hertz.
Soundwaves move through many different materials by means of particle displacement in the molecular structure.

## Slide 14: Velocity of sound energy within material
  Sound waves travel through material by transferring mechanical energy from one atom to the next as detailed in this simple illustration.
  The more densely packed the atoms are arranged, the faster the sound energy travels through the material.

## Slide 15: The typical Pulse-echo instrument technique

## Slide 16: The makeup of an ultrasonic transducer
The transducer must be able to perform two functions:
  Convert electrical energy to mechanical energy.
  Convert mechanical energy to electrical energy.

## Slide 17: Ultrasonic wave modes
Ultrasonic waves can be categorized in four different wave modes. Each wave mode has a different effect on the particle displacement and limitations when performing various inspections.
  Longitudinal (Compression) waves
  Shear (Transverse) waves
  Surface (Raleigh) waves
  Plate (Lamb) waves

## Slide 18: Longitudinal or Compression waves
Primarily used to determine:
  material soundness examinations
  Material thickness examinations

## Slide 19: Shear or Transverse waves
Primarily used to detect small discontinuities in material. This wave type is typically used to inspect welds for flaws.

## Slide 20: Surface or Raleigh waves
Used to test surface discontinuities in material.

## Slide 21: Plate or Lamb waves
Used to ultrasonically inspect thin gage sheet material for discontinuities.

## Slide 22: Sound
Longitudinal Wave

## Slide 23: Pitch
Determined physically by frequency
“Audible Range” = 20 to 20000 Hz
Above 20,000Hz, ultrasonic
Below 20Hz, infrasonic

## Slide 24: Graphing Compression Waves

## Slide 25: Sound Pitch, Graphically

## Slide 26
Wind Instruments
Cause sound by standing waves in a column of air
Vibration caused by reed, player’s lips, or turbulence

## Slide 27: Closed at One End
For ¼ wave:
  V = wavelength x frequency
  Wavelength = 4(L + 0.4D)
D
L